QYT KT-8900 Quick Reference
(6) [Power]: Press and hold to turn on and off. / (12) [V/M] / Press to toggle between VFO and Memory Channels. / Use the knob (1) to change frequencies or channels or / Use the Up / Down arrows on the mic, or / Key in a number on the mic. For channels, it’s better to key in a 3-digit number (ex. Ch. 12 would be “012”) / (11) [EXIT / AB] / Press to toggle between receiver A and B. / Note where the arrow is on the left of the screen.	(12) [VFO]: on the fly “programming”: / Select a receiver A/B / Key in a frequency. / (3) [F] (or [MENU] on mic). In the menu: / use the UP / DOWN arrow to navigate to a setting / press [F] / [MENU] again until the setting flashes, then the UP / DOWN arrow to change the setting. / press [F] / [MENU] again to activate the change. / Menus to change for repeater use: / 3 – TX power (Low / High) / 11 – Rx tone (tone squelch is optional) / 13 – Tx tone (tone required by the repeater) / 38 – Repeater offset direction (+ / - ) / 39 – Repeater offset (VHF: “00600” / UHF: “05000”) / Press (11) [EXIT / AB] to exit the menu. / These settings will stay applied to the VFO receiver (A/B) initially selected (but not the other one) even if you change the frequency. / To go back to simplex, the same settings will have to be changed back. / This radio has 200 channels.