AT-100ProII Autotuner Quick Reference
Operation / Func: Activates secondary function of other buttons. / Ant: Selects the active antenna port. / C Up: Manually increase capacitance. / C Dn: Manually decrease capacitance. / L Up: Manually increase inductance. / L Dn: Manually decrease inductance. / Tune: / Momentary push places tuner in bypass. / Medium Press > 0.5 sec initiates a memory tuning cycle / Long Press > 2.5 sec initiates a full tuning cycle. / Func – Peak: Displays average power (for 100% duty cycle modes) or peak power (for varying duty cycle modes) / Func – Scale: Toggles the bargraph display between in 0-12.5 and 0-125 watt ranges. / Func – Auto: Toggles between automatic and semi-automatic modes / Func – Thresh: Sets the threshold for the automatic tuner to kick in	Error Codes / ERR_NO_MATCH: Unable to find a suitable match below 3.5:1. / ERR_NO_RF: No RF power was present at the beginning of a tuning cycle. / ERR_LOST_RF: RF power disappeared before the tuning cycle completed. / ERR_NO_FREQ: Unable to determine operating frequency. / ERR_SWR_PWR: Relay protection activated. Relays will not toggle if the SWR is over 3.0:1 while the power is over 125 W.