Baofeng UV-5R Quick Reference
(3) [Power / Volume]: Turn the knob to turn on and off. / (8) [VFO/MR] / Press to toggle between VFO and Memory Channels. / Use the Up / Down to change frequencies or channels or / Key in a number on the mic. For channels, it’s better to key in a 3-digit number (ex. Ch. 12 would be “012”) / (12) [A/B] / Press to toggle between receiver A and B. / Note where the arrow is on the left of the screen. / [*] / Short press to reverse repeater output and input / Long press to scan channels or frequencies / [#] / Short press to toggle between H/L power / Long press to lock the controls	(8) [VFO/MR]: on the fly “programming”: / Enter the VFO mode. / Select a receiver A/B / Key in a frequency. / (14) [MENU] In the menu: / use the UP / DOWN arrow to navigate to a setting / press [MENU] again until the setting flashes, then the UP / DOWN arrow to change the setting. / press [MENU] again to activate the change. / Menus to change for repeater use: / 2 – TX power (Low / High) / 11 – Rx tone (tone squelch is optional) / 13 – Tx tone (tone required by the repeater) / 25 – Repeater offset direction (+ / - ) / 26 – Repeater offset (VHF: “00600” / UHF: “05000”) / Press (14) [EXIT] to exit the menu. / These settings will stay applied to the VFO receiver (A/B) initially selected (but not the other one) even if you change the frequency. / To go back to simplex, the same settings will have to be changed back. / This radio has 128 channels.