Icom 207H Quick Reference
(5) [Power]: Press and hold to turn on and off. / Buttons 13 – 8 each have at least two functions: / press and hold to access the upper function in bold / press and release to access the lower function / (13) [V/MHz] / Press and release for VFO. Knob (1) changes the frequency. / Press and release again and knob (1) changes Mhz. / Press and hold to scan. / (3) [BAND] / In VFO mode, there are four bands / 118.000 – 136.000 MHz (Air) / 136.000 – 174.000 MHz (2m) / 320.000 – 400.000 MHz / 400.000 – 479.000 Mhz (70cm) / (12) [MR]: / Select Memory Chanel mode. / Press again to change to Call Channel.	(13) [VFO]: on the fly “programming”: / To change band (Air, 2m, 300, 70cm) / Press(3) [BAND] / To add a tone: / Press (11) [TONE] to activate the tone then / Press (8) [SET] multiple times to navigate the menu and changes “rt” and “ct” using the knob (1) / Press (13) [V/MHz] to exit. / To force a different offset: / Press and hold (10) [DUP] as needed. / To change tx power: / Press (10) [LOW] to toggle: LO (5W), LO-MID (10W), MID-H (20W), H (50W / 35W) / To listen to the input of a repeater: / Press (9) [MONI] / To store a VFO frequency to a memory channel: / Setup frequency, tone, and offset in VFO / Press (2) [MW S.MW]. The channel will flash. / Select the desired channel with the knob (1) / Press and hold (2) [MW S.MW] / Press (12) [MR] to switch to channel mode. / This radio has 150 channels.