QYT KT-8900 Menu
#	Label	Description	Possible Values	Set to	Details
0	TDR	Transmit Dual Receive	ON	Off for Digital / On or Off for voice	Allows monitoring of 2 channels. Toggles between Freq A and B. If signal received, RX stays on Freq.
			OFF		Receives on selected channel
1	STEP	Frequency Step Size Setup	2.5 to 25. kHz	5	5, 6.25, 10, 12.5, 15, 25 kHz
2	SQL	Squelch Level	00 > 09	2	10 squelch levels 00 = minimum / normally open
3	TXP	Transmit Power	High	Low for Digital	Full Power
			Low		Reduced Power
4	SCR	Voice Scrambler Does Not function on version 1 radio's	ON	OFF (not legal for ham radio)	Activate Scrambler Function
			OFF		Deactivate Scrambler Function
5	TOT	Time Out Timer	15 > 600 secs	600	15 second steps
6	TOA	Transmit Over Alarm Setting (TOT Warning)	1 > 10 seconds	5	Amount of time the indicator light flashes prior to time out
			OFF		Turn off the flashing indicator
7	WN	Bandwidth	Wideband		25.0 kHz
			Narrowband		12.5 kHz
8	ABR	LCD Backlight Timer	1 > 50 secs	OFF	Backlight duration = 1 > 50
			OFF		Disables 1 > 50 second timer. Backlight remains ON.
9	BEEP	Keypad Voice Prompt	ON / OFF	OFF	Turn ON / OFF keypad voice prompt
10	R-DCS	Receive - Digital Coded Squelch	D023N > D754I		Squelch opens when proper DCS code is detected
			OFF		No DCS code required
11	R-CTCS	Receive - Analog Tone Squelch	67.0 > 254.1 Hz		Squelch opens when proper CTCSS tone detected
			OFF		No CTCSS tone required
12	T-DCS	Transmit - DCS Code	D023N > D754I		Transmits specified code
			OFF		No DCS code transmitted
13	T-CTCS	Transmit - CTCSS Code	67.0 > 254.1 Hz		Transmits specified tone
			OFF		No CTCSS tone transmitted
14	DTMFST	Determines when DTMF codes are heard through speaker	OFF		No DTMF tone heard
			KEY	BOTH	Only manually keyed DTMF codes are heard
			ANI		Only automatically keyed DTMF codes are heard
			BOTH		All DTMF codes are heard
15	BCL	Busy Channel Lockout	ON	OFF	Prevents transmit if active signal on the channel
			OFF		No lockout
16	SC-ADD	Add Scan Channel	ON		Add channel to scan list
			OFF		Remove channel from scan list
17	PRI-SC	Priority Scan	ON		Activate Priority Scan
			OFF		Deactivate Priority Scan
18	PRI-CH	Priority Channel	000 > 199		Channel selected for Priority Scan
19	SC-REV	Scan Resume Method	TO	CO	-- TO (Time Operation) Scan stops when signal detected. Scan resumes after approx 5 seconds (even if the channel is still active)
			CO		(Carrier Operation) Scan stops when signal detected. Scan resumes when signal disappears.
			SE		(Search Operation) Scan stops when signal detected. Scanning will not resume.
20	OPTSIG	Optional Signaling	OFF	OFF	No optional signaling
			DTMF		DTMF signaling selected
			2TONE		2TONE signaling selected
			5TONE		5TONE signaling selected

21	SPMUTE	Speaker Mute Settings	QT	QT	Squelch opens for CTCSS/DCS tones only.
			AND		Squelch opens when CTCSS/DCS tone is recognized along with the optional signaling.
			OR		Squelch opens when either the CTCSS/DCS tone OR the optional signaling is recognized.
22	PTT-ID	PTT ID - When to send	OFF	OFF	Do not send
			BOT		Send at Beginning of Transmission
			EOT		Send at the End of Transmission
			BOTH		Send at both Beginning and End
23	PTT-LT	PTT ID - Transmit Delay	0 > 30		Set Delay Time before transmitting PTT-ID
24	S-INFO	Auto Group Dialing	Group Signal Code Memory		1 > 15 Can only be set with software
25	EMC-TP	Alarm Mode	ALARM	BOTH	Turn on Alarm sound
			ANI		Send Alarm code and ID code
			BOTH		Both of the above
26	EMC-CH	Alarm Channel	000 > 199		Specified Alarm Channel
27	RING-T	Ring Time	OFF, 1 > 10	3	OFF - No Ring Time
					1 > 10 seconds ring time when signal code received
28	CHNAME	Channel Name Edit	In Channel Mode, edit the Current Name
29	CA-MDF	A Channel Display Mode	FREQ		In Channel Mode, display the selected format in display A
			CH
			NAME
30	CB-MDF	B Channel Display Mode	FREQ		In Channel Mode, display the selected format in display B
			CH
			NAME
31	AUTOLK	Automatic Lockout	OFF	OFF	Open Keypad Function
			ON		Lock the Keypad
32	PONMSG	Power On Message	FULL		Full Screen Display
			MSG		Show Power On Message
			BATT-V		Display Battery Voltage
33	WT-LED	Standby - Backlight Color Selection	OFF		Select desired color
			BLUE
			ORANGE
			PURPLE
34	RX-LED	Receive - Backlight Color Selection	OFF		Select desired color
			BLUE
			ORANGE
			PURPLE
35	TX-LED	Transmit - Backlight Color Selection	OFF		Select desired color
			Blue
			ORANGE
			PURPLE
36	MEMCH	Memory Channel	000 > 199		Indicates channel number to be stored. "CH" will appear after channel is stored.
37	DELCH	Delete Channel	000 > 199		Indicates channel number to be deleted. "CH" will disappear after channel is deleted.
38	SFT-D	Frequency Shift Direction	OFF		No Offset (simplex)
			+		Plus frequency shift
			-		Minus frequency shift
39	OFFSET	Frequency Shift Offset Amount	00.00 > 69.99		Frequency shift in MHz
40	ANI	ANI ID Code	Can only be set with software
41	ANI-L	ANI Length	3, 4, 5		Length of ANI ID code
42	REP-S	Repeater Activation Tone	1000Hz / 1450Hz / 1750Hz / 2100Hz		Audible tone for repeater activation.
43	REP-M	Repeater Forwarding Mode	OFF		Function OFF.
			CARRI		Forward after receiving Carrier.
			CTDCS		Forward after receiving correct CTDCS.
			TONE		Forward after receiving correct mono audio (Menu 42)
			DTMF		Forward after receiving assigned DTMF code.
44	TDR-AB	Dual standby function setup	OFF	OFF	Radio always stay on the main band.
			1-50		Radio will automatically switch to the receiving channel for n seconds.
45	STE	Squelch tail-elimination setup	ON	OFF	Enable.
			OFF		Disable. Use this if working with a repeater.
46	RP-STE	Repeater squelch tail elimination setup	OFF	OFF	Disable.
			1-10		Squelch tail length used to eliminate tail noise produced by repeater delay.
47	RPT-DL	Delay time to receive repeater signal setup	OFF	OFF	Disable.
			1-10		Delay time to receive repeater signal.
48	RESET	Initialize to Factory Defaults	VFO	ALL	Menu Initialization.
			ALL		Menu and Channel Initialization.