Kenwood TM-D710G Quick Reference
(pp. 8-9) / (16) [Power]: Press and hold to turn on and off. / (12) [BAND SEL]: / Left and right volume and squelch controls Side A and Side B receivers respectively. / To select a side to control or tx, press the left or right [BAND SEL]. Note where “PTT CTRL” is on the screen: / Press and hold to switch to and from single band. (p.20) / (4) [Tuning control] / Tunes the frequency or channel of the selected / Press in VFO mode to select MHZ group to tune / Press for 1s to scan frequencies or channels / (2) [VFO] / (3) [MR]: / Select VFO or Memory Chanel mode. / Hold to scan (same as holding (4) )	(2) [VFO]: on the fly “programming”: / To change band (Air, 2m, 440, 1200): (p.20) / Press (6) [F] followed by / the appropriate (12) [BAND SEL] button / Side A has: 118-136, 136-200, 400-524 / Side B has: 136-200, 400-524, 800-1300 / To add a tone: / Press (7) [TONE] to activate the tone then / Press (6) [F] followed by (7) [T.SEL] / Then turn (4) [Tuning Control] to select the right tone. / Then press (4) [Tuning Control] to save the selection. / To change tx power: / Press (9) [LOW] to toggle L(5W), M (10W), H (50W) / To listen to the input of a repeater and transmit on its output: / Press (8) [REV] / To change the control side without changing the PTT side: (p.19) / Press (11) [PF2]